## Slide 1: Introduction to AVR

## Slide 2: Topics
Microprocessors vs. Microcontrollers
Most common microcontrollers
AVR Features
AVR members

## Slide 3: Microprocessors vs. Microcontrollers
Microprocessors (General Purpose)
Microcontrollers

## Slide 4: Why Microcontroller
Microcontrollers are important part of Embedded
Systems
To understand structure and working of
microcontroller
For designing good Embedded system complete
understanding of microcontrollers is required.

## Slide 5: Microcontroller
Integrated chip that typically contains integrated CPU, memory(RAM,ROM),I/O ports on a single chip
Basically system on chip
Designed to execute specific task to control a single system

## Slide 6: AVR Microcontroller
AVR stands for Advanced Virtual RISC
  the founders are Alf Egil bogen Vegard wollen RISC
  AVR architecture was conceived by two students at Norwegian institute of Technology and further refined by Atmel Norway.

## Slide 7: RISC Advantages
Fast execution of instructions due to simple instructions for CPU
RISC requires fewer transistor which makes the design cheaper.
Emphasis on software
Single clock instructions only
Register to Register: LOAD and STORE are independent instructions

## Slide 8: AVR Microcontroller
A series of 8-bit RISC microcontrollers from Atmel.
All AVR microcontroller share same instruction set basic CPU(Harvard) architecture
It has 32, 8bit general purpose registers.
Mostly instructions get executed in single cycle.

## Slide 9: AVR Which you have already learnt
Operating Voltage: 5V
Input Voltage : 7v to 12V
14 Digital I/O pins
6 Analog I/O pins
Flash Memory is 32 KB
SRAM is 2 KB
EEPROM is 1 KB
CLK Speed is 16 MHz
DC Current for I/O pins is 40 mA
DC Current for 3.3V Pin is 50 mA

## Slide 10: AVR Types
Classic AVR
  e.g. AT90S2313, AT90S4433
Mega
  e.g. ATmega328, ATmega32, ATmega128
Tiny
  e.g. ATtiny13, ATtiny25
Special Purpose AVR
  e.g. AT90PWM216,AT90USB1287
XMega
  New features like DMA, DAC, crypto engine, etc.

## Slide 11: AVR internal architecture

## Slide 12: AVR’s CPU
AVR’s CPU
  It’s an 8-bit Microcontroller
  ALU
  32 General Purpose registers (R0 to R31)
  PC register
  Instruction decoder
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 13: Data Address Space

## Slide 14
ATmega32 ports are 8-bit SFRs
Port A, Port B, Port C and Port D
Configurable as
    Input Port
    Output Port
    Alternate Function
AVR Ports

## Slide 15: Port Register Functions
Port has 3 registers (8-Bit each)
  PORTx (Output Data)
  DDRx (Direction of Data)
  PINx (Input Data)

## Slide 16: Port Internal Structure
Upon reset, all ports have the value 0x00 in their DDR registers. This means that all ports are configured as input

## Slide 17
Alternate functions of Port A and Port B

## Slide 18
Alternate functions of Port C and Port D